## Slide 1
[University of Central Lancashire]

## Slide 2: Topics
Blade design according to Betz
Blade design according to Schmitz
Blade design for recent variable speed turbines
Implementation in NREL codes
Summary
No reproduction, publication or dissemination of this material is authorized, except with written consent of the author.
Oldenburg, May 2016 Prof. Dr. Martin Kühn

## Slide 3: Overview
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes
Blade design for recent variable speed turbines

## Slide 4: The design of a typical wind turbine blade.
http://www.reinforcedplastics.com/view/3144/curing-agents-improve-rotor-production/ (accessed 14 May 2014)
Note:
We are dealing only with the aerodynamic blade design here! In reality, aerodynamic design and structural design and production and logistics are strongly interrelated design aspects.

## Slide 5: 1. Blade design according to Betz NACA profile series
National Advisory Committee for Aeronautics
Public available blade profile data
Different families of profiles, defined by number of digits
More information can be found in the internet

## Slide 6: Find optimal lift coefficent
Optimal lift coefficient is defined as maximum of the lift-to-drag ratio
Still good lift-to-drag ratio at higher angles of attack
Different Cp can be desired if max. lift-to-drag ratio leads to smaller Cp’s
  Larger Cp  smaller blade chord
Chart: Angle of attack
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 | 9.5 | 10.0 | 10.5 | 11.0 | 11.5 | 12.0 | 12.5 | 13.0 | 13.5 | 14.0 | 14.5 | 15.0 | 15.5 | 16.0 | 17.0 | 17.5 | 18.0 | 18.5 | 19.0 | 19.5 | 20.0 | 20.5 | 21.0 | 21.5 | 22.0
Lift coefficient | 0.1858 | 0.2451 | 0.3042 | 0.3629 | 0.4216 | 0.4798 | 0.5378 | 0.5937 | 0.6486 | 0.7018 | 0.7542 | 0.8072 | 0.86 | 0.9135 | 0.9674 | 1.0219 | 1.0749 | 1.128 | 1.1811 | 1.2311 | 1.2826 | 1.3297 | 1.3776 | 1.4219 | 1.4597 | 1.4928 | 1.526 | 1.554 | 1.5776 | 1.5965 | 1.6102 | 1.6167 | 1.6111 | 1.6283 | 1.6371 | 1.6412 | 1.6397 | 1.6359 | 1.626 | 1.6123 | 1.5939 | 1.5705 | 1.5385 | 1.498
Drag coefficient | 0.00474 | 0.00477 | 0.00479 | 0.00489 | 0.00495 | 0.00511 | 0.00525 | 0.00566 | 0.00618 | 0.00692 | 0.00775 | 0.00847 | 0.00922 | 0.0098 | 0.0103 | 0.01069 | 0.01121 | 0.01169 | 0.01212 | 0.01283 | 0.01328 | 0.01407 | 0.0147 | 0.01551 | 0.0166 | 0.01736 | 0.01846 | 0.01995 | 0.02182 | 0.02413 | 0.02696 | 0.03054 | 0.03531 | 0.04342 | 0.04784 | 0.05315 | 0.05953 | 0.06652 | 0.0746 | 0.08378 | 0.09421 | 0.10593 | 0.11977 | 0.13589
Chart: Angle of attack
Lift to drag ratio | 39.1983 | 51.3836 | 63.5073 | 74.2127 | 85.1717 | 93.8943 | 102.4381 | 104.894 | 104.9515 | 101.4162 | 97.3161 | 95.3011 | 93.2755 | 93.2143 | 93.9223 | 95.594 | 95.8876 | 96.4927 | 97.4505 | 95.9548 | 96.5813 | 94.506 | 93.7143 | 91.6763 | 87.9337 | 85.9908 | 82.6652 | 77.8947 | 72.3006 | 66.1625 | 59.7255 | 52.9371 | 45.6273 | 37.5012 | 34.2203 | 30.8786 | 27.5441 | 24.5926 | 21.7962 | 19.2444 | 16.9186 | 14.8258 | 12.8455 | 11.0236
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes

## Slide 7: Determination of blade planform t(r) acc. to Betz, i.e. excluding wake rotation
Objective: optimum local wind speed reduction
Assumption: lift >> drag at design point
power from blade element (BE) theory = max. power
(Betz)
dr
r
thrust
(at blade)
peripheral
force
rotor plane
rotor axis
Relative speed, Vrel
inflow angle, a
lift
blade speed, Wr
inflow, V2

## Slide 8: Determination of blade twist
Objective: optimum local wind speed reduction
Assumption: lift >> drag at design point
Power from blade element theory = max. power (Betz)
atwist
rotational plane
vrel
aA
A(r)
rotor chord
rotor axis
v2
W
W r
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes
!

## Slide 9: Formula for chord and twist acc. to Betz
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes

## Slide 10: 2. Blade design according to Schmitz, i.e. including wake rotation

## Slide 11: Dimensionless planform: Betz vs. Schmitz:

## Slide 12: Blade twist: Betz vs. Schmitz

## Slide 13: Overview
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes
Blade design for recent variable speed turbines

## Slide 14: Traditional choice of design tip speed ratio D for turbine with (almost) constant rotor speed
D=1
D=2
D=6
D=8
D=11
[fig. Gasch]
D  1 : Wind energy converter of low rotational speed (prime mover)
D > 5 : Wind energy converter of high rotational speed (turbine)

## Slide 15: (Dimensionless) rotor solidity σ Ratio of rotor surface to swept rotor area
[fig. Gasch]
with:
average chord length
turbine with low tip speed ratio
(N = 20, λD = 1): σ = 100 %
turbine with low high tip speed ratio
(N = 2, λD = 8): σ = 4 %
N

## Slide 16: Distribution of blade chord and twist for different design tip speed ratio D
Note: In the diagram λ is referring to the design tip speed ratio λD
[fig. Gasch]

## Slide 17: 4. Blade design for recent variable speed turbines
[Source: www.eyeofthefish.org]
Example: Development of Enercon blade designs
[Source: Gasch, 2015]

## Slide 18: Power limitation & control
vcut-out
Elec. power
Pitch angle
Wind speed
vcut-in
vrated
vcut-out
Rotor speed
85o
65o
25o
0o
Region 1 Region 2
4m/s
11 - 13m/s
20-25m/s
nnenn
λ = λopt
λ < λopt
λ « λopt
below Vcut-in (approx. 3 – 4 m/s) :
idling, large pitch angle
Region 1: betw. Vcut-in and Vrated (approx. 11 – 12 m/s) :
production at partial load
pitch angle constant at 0o
variable speed proportional to wind
turbine operating at aerodyn. optimum
Region 2: betw. Vrated and Vcut-out (approx. 20 - 25 m/s) :
production at full load
speed on average constant
pitch angle increases with wind
dynamic control of speed (fast) and pitch
(slower) to reduce power and load
variations
above Vcut-out : idling, large pitch angle
Standstill Start Partial load Full load Cut-out
Idling No pitching Pitch control Idling
var. speed nrated ±10%

## Slide 19: Power, Cp and CT curves: E-101 3050 kW
var. speed
var. pitch

## Slide 20: Different blade design philosophies of var. speed WT
Exp 1: Very traditional design
=> tapered chord, moderate design tip speed => relative high solidity
Exp. 2: Enercon E-101 3,050 kW (series production: Aug 2011)
=> slender blade, design for var. rotor speed, D  7,7
Exp. 3: Enercon E-115 3,000 kW (series production: mid 2014)
=> very slender blade, design for var. rotor speed, D  9,5
[Source: Enercon Windblatt 04/2012, p. 14]
[Source: www.eyeofthefish.org]

## Slide 21: Power curves for different spec. rating (W/m2)
Chart: Wind speed [m/s}
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0
E-115: 3000 kW | 0 | 3 | 48.5 | 155 | 339 | 627.5 | 1035.5 | 1549 | 2090 | 2580 | 2900 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000
E-101: 3050 kW | 0 | 3 | 37 | 118 | 258 | 479 | 790 | 1200 | 1710 | 2340 | 2867 | 3034 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050 | 3050
E-82 E4: 3000 kW | 0 | 0 | 25 | 82 | 174 | 321 | 525 | 800 | 1135 | 1510 | 1880 | 2200 | 2500 | 2770 | 2910 | 3000 | 3020 | 3020 | 3020 | 3020 | 3020 | 3020 | 3020 | 3020 | 3020
E-70 E4: 2300 kW | 0 | 2 | 18 | 56 | 127 | 240 | 400 | 626 | 892 | 1223 | 1590 | 1900 | 2080 | 2230 | 2300 | 2310 | 2310 | 2310 | 2310 | 2310 | 2310 | 2310 | 2310 | 2310 | 2310
285 m2
381m2
572 m2
583 m2

## Slide 22: Examples of different industrial design approaches for modern slender blades
80% Schmitz design [Gasch, 2015]
Design blade for common D value
Reduce the chord length to 80%
Compute Cp-, Cm- and CT- curves with BEM code for given blade design
Determine optimum  , which will be higher than initial D
Design for high D in the variable speed range
Design blade directly for higher D
 and hence Cp will decrease significantly in the constant rotor speed range in the upper partial load regime
Internal company know-how and procedures
…

## Slide 23: Different blade design philosophies of var. speed WT
Exp. 2: Enercon E-101 3,050 kW (series production: Aug 2011)
=> slender blade, design for var. rotor speed, D  7,7
Exp. 3: Enercon E-115 3,000 kW (series production: mid 2014)
=> very slender blade, design for var. rotor speed, D  9,5
[Source: Patent »Rotorblatt einer Windenergieanlage«
DE 102012206109 B3]

## Slide 24: Schmitz design for different D
At constant D chord is proportional to R and 1 / (r/R)
=> larger blades require more chord (see E-101 D= 7.7 vs. E-115 D= 7.8)
Increase of D reduces chord proportional to 1 / (D)2
=> slender blade with high D (see E-101 D= 7.7 vs. E-115 D= 9.7)
Increase of design lift coefficient linearly reduced chord
=> Cl,d > 1 might cause problems at turbulent sites or with rough airfoils

## Slide 25: Power and  against wind speed
var. speed range
Enercon E-115
(TSR=9.7)
var. speed range
Enercon E-101
(TSR=7.7)
E-115 (77,5 m/s) maintains almost same maximum tip speed as E-101 (76,7 m/s)
=> variable rotor speed only a low and medium partial load range until max. tip speed is reached

## Slide 26: Penalty on power coefficient for  < D
var. speed range: E-115
var. speed range: E-101
var. speed range: E-70 E4

## Slide 27: Effect of poor Cp on power curves

## Slide 28: Effect on energy yield (E-115 vs. E-101) (+12% AEP from 31% larger swept area at vave = 7 m/s)
Enercon E-115 (3000 kW)
Enercon E-115 (3000 kW)
115 m

## Slide 29: http://wind-data.ch/tools/powercalc.php?lng=en

## Slide 30: Distribution of relative blade thickness along the blade span

## Slide 31: Overview
Blade design (Betz)
Blade design (Schmitz)
Implementation in NREL codes
Blade design for recent variable speed turbines

## Slide 32: Complete rotor design
Open tab „Blade_geometry“ of „CIP_01_DoWES.Rotor_design_start_parameter.SS2014.01.xlsx“
Calculate blade properties
Verify twist and chord distribution
1
3
2

## Slide 33: Simulation – Several modules

## Slide 34: Simulation – Onshore
Onshore wind turbine

## Slide 35: Simulation – AeroDyn
TurbSim
AeroDyn
FAST
Onshore wind turbine
See manuals:
“AeroDyn_UserGuide.pdf”
“AeroDyn_Theory.pdf “

## Slide 36: Aerodynamics – Input file for AeroDyn
Rename input file „Blade_Color_Aero.ipt“ with the „color“ of your turbine (example: blue, green, red, etc.)
Open renamed file & inspect information:
1
2

## Slide 37: Aerodynamics – Input file for AeroDyn
Rename input file „Blade_Color_Aero.ipt“ with the „color“ of your turbine (example: blue, green, red, etc.)
Open renamed file & inspect information:
  aerodynamic calculation
  turbulent wind field file
  Hub height & air properties
  Airfoil files & blade geometry
1
2

## Slide 38: Aerodynamics – Blade design

## Slide 39: Aerodynamics – Update AeroDyn
Write hub-height
Complete name & path of airfoils: „NACAyy_xxx“, „RISOExx_yy“
Enter rotor blade definition:
  RNodes – distance from root
  AeroTwist – twist angle
  DRNodes – element length
  Chord – chord length
Check „AeroDyn_UserGuide.pdf“
3
5
4

## Slide 40: Summary / Conclusion
We designed our own blades with respect to the given start parameters
Results: blade planform and twist for Betz and Schmitz design methodology
Chart: Planform
| 0.0 | 3.609375 | 10.828125 | 18.046875 | 25.265625 | 32.484375 | 39.703125 | 46.921875 | 54.140625 | 57.75
Betz | 16.6557 | 15.8957 | 8.631 | 5.6834 | 4.2047 | 3.329 | 2.7526 | 2.3454 | 2.0426 | 1.9187
Schmitz | 3.3623 | 7.0238 | 5.7692 | 4.1725 | 3.1905 | 2.5642 | 2.1374 | 1.8298 | 1.5985 | 1.5032
Chart: Twist
| 0.0 | 3.609375 | 10.828125 | 18.046875 | 25.265625 | 32.484375 | 39.703125 | 46.921875 | 54.140625 | 57.75
Betz | 66.5938 | 37.1826 | 13.471 | 5.2044 | 1.188 | -1.1634 | -2.7024 | -3.7867 | -4.5913 | -4.9204
Schmitz | 43.9809 | 28.8638 | 12.0512 | 4.786 | 1.0164 | -1.249 | -2.751 | -3.8168 | -4.6112 | -4.9369

## Slide 41: Reserve: --- no pdf, don‘t print ---

## Slide 42: 1. Introduction to CIP Tutorials
Rotor design
Characteristic curves
Turbine dynamics
External conditions
Load analysis
Main parameters

## Slide 43: Groups
Nr. | Color | Student 1 | Student 2 | 
1 | Red |  |  | 
2 | Green |  |  | 
3 | Blue |  |  | 
4 | Yellow |  |  | 
5 | Pink |  |  | 
6 | Turquoise |  |  | 
7 | Orange |  |  | 
8 | Black |  |  | 
9 | Violett |  |  | 
10 | Grey |  |  |